## Slide 1
3
AQA
    GCSE
      Design and Technology 8552
Commercial manufacturing,
treatments and finishes
Unit 5B
  Timber based materials

## Slide 2
Objectives
Know and understand how timbers and boards are selected and processed for commercial products
Learn how materials are cut, shaped and formed to a tolerance
Learn about the preparation and application of treatments and finishes to enhance functional and aesthetic properties

## Slide 3
Manufactured boards
Identify the types of manufactured board shown below and suggest a use for each one

## Slide 4
Engineered wood
Manufactured or engineered wood has many advantages over solid wood
  May be mixed with glues to give greater strength and stability
  Ideal for use in construction, industrial and domestic use
  Efficient in its use of mixed materials and utilising waste wood
  It can be made in a large sheets not limited by the diameter of a tree trunk
What would be three disadvantages of using man made board?

## Slide 5
Flat-pack furniture
Manufactured boards are well suited to self-assembly products
  They are generally less expensive than hand-made items
  Arrives boxed making it easier to store and transport
  Relatively straightforward to assemble with a basic tool kit
  What properties of manufactured board make it suitable for flat-pack products?
  Why do you think it may be less aesthetically appealing?

## Slide 6
Choice of material
A day in the life of a child’s toy is a tough one!
  They are thrown, dropped in water, left outside, stood on and chewed
  Justify a suitable type of wood to make a child’s toy

## Slide 7
Natural or man-made
The type of material a product is made from will also influence the price of the end product
  Similar products may be made from different timbers to appeal to different markets
  Some timbers are traditionally used for certain products
  Which timber would you select to make a gate? Give two reasons why?

## Slide 8
Worksheet 3
Complete Task 1 of the worksheet

## Slide 9
Commercial manufacturing
Mass produced timber components are produced using CNC machinery
  This enables large quantities of equal- sized parts or products to be produced
  Templates can be saved and reused to help minimise waste
  Screw holes, slots and patterns can be cut in one process
  What are the benefits to the manufacturer of minimising waste?
  How could they dispose of the waste responsibly?

## Slide 10
Commercial routing
CNC machinery can cut, drill, shape, mill and profile manufactured or natural timbers
  Screw holes, slots and patterns can all be cut in one process
  Machines can accommodate big sheets of material
  Machines work quickly and efficiently enabling a product to get to market swiftly
  What other advantages does CNC routing offer over hand cutting?

## Slide 11
Commercial turning
CNC wood lathes produce cylindrical components
  Once programmed they are very effective at producing complex shapes and spirals
  Ideal for repeat production
  Lathes can accept large and long pieces of material
  What disadvantages would the introduction of CNC machinery present to a skilled workforce?

## Slide 12
Routing and turning
These techniques are used to produce many day to day items
  Think of five more examples

## Slide 13
Mechanisation and automation
Automated machinery has changed the way industry manufactures timber based products
  Improvements in manufacturing methods have been embraced by designers
  Stringent quality control methods have increased consistency and accuracy
  Increased availability of manufactured boards means products can be batch and mass produced
Discuss the differences between ‘mechanisation’ and ‘automation’

## Slide 14
Quality Control – ‘QC’
The process where products are checked to ensure they meet the design specification
They should also:
  function correctly
  be free of defects
  be consistent and accurate
  meet set size tolerances
  Make a sketch of the wooden shape sorter and compile your own QC checklist listing the key areas to check

## Slide 15
Tolerance
The total amount a specific dimension or property is permitted to vary
  This can apply to hole depth, length, angle, thickness, weight and elasticity
  A gauge can be inserted into a gap or hole to check if the sizes fall within tolerance
  If parts do not fit within the specified tolerances they are discarded or recycled
  Why is it important for a manufacturer to ensure they have rigorous quality control systems in place?

## Slide 16
Go / No Go?
The required thickness for a table leg in a flat packed table is 25mm
Four legs are measured. The tolerance is +/- 0.5mm
Are they Go or No Go?
  Leg 1: 25.46mm
  Leg 2: 24.42mm
  Leg 3: 25.51mm
  Leg 4: 24.68mm

## Slide 17
Go / No Go?
The required thickness for a table leg in a flat packed table is 25mm
Four legs are measured. The tolerance is +/- 0.5mm
Are they Go or No Go?
  Leg 1: 25.46mm Go
  Leg 2: 24.42mm No Go
  Leg 3: 25.51mm No Go
  Leg 4: 24.68mm Go
  What are the consequences if the table leg doesn’t fit within the tolerance?

## Slide 18
Surface treatments and finishes
Wood can be protected and visually enhanced using:
  Preservative
  Wax
  Oil
  Paint
  Stain
  Varnish
Finishes can be applied by brushing, rubbing or spraying
  What treatments and methods would you use to finish a garden shed, a toy wooden boat and a cricket bat?

## Slide 19
Enhancing the appearance
As well as improving the function, finishes can make a product more appealing
  How would you enhance the natural grain of wood?
  Why would you choose to paint a child’s toy rather than leaving it bare?

## Slide 20
Wood preservation
Treating timber can help extend its life for decades
Tanalising is the process in which timber is immersed in a preservative
  Hydraulic pressure forces the treatment deep into the timber
  Helps delay the rotting process
  Protects against insect and fungal attack
  Where might you find tantalised timber in use?

## Slide 21
Commercial finishing
Modern finishes can extend the life of timber based products
  Products can be sprayed by hand or machine
  Patterns, logos or wording can be printed onto the surface
  One of the fastest ways of painting is using a ‘curtain coater’ which gives a smooth and even coat
  What are the advantages of applying a finish on a production line?

## Slide 22
Environmental impacts
Traditional paints and finishes can have harmful effects on the environment
  Oil or solvent based products offer long lasting finishes, but contain high levels of VOCs – Volatile Organic Compounds
  Water based products are kinder to the environment
  Paint can be made from recycled latex and even milk
  What items of PPE would you use when using a solvent based finish on a wooden floor?

## Slide 23
Worksheet 3
Complete Task 2 on the worksheet

## Slide 24
Plenary
What factors would a furniture manufacturer consider when selecting a material to make flat-pack furniture?
How has machinery improved the production of mass produced timber components?
Why are tolerances so important to check as part of the quality control process?
Which products help protect or improve the aesthetics of timber based materials?