## Slide 1
1
AQA
    GCSE
      Design and Technology 8552
Sources, origins and properties
Unit 5D
  Polymers

## Slide 2
Know the primary sources of polymers
Understand the processes involved in refining, fractional distillation and cracking to produce workable forms of polymers
Understand how plastics can be modified to enhance their properties
Be aware of sustainability and ethical issues in plastics production, in use and end of life
Objectives

## Slide 3
What is plastic?
The word plastic means ‘easily shaped or moulded’ and is derived from the Greek work ‘plastikos’
Plastics are made from polymers which is a Greek word meaning many: ‘poly’ - parts: ‘mer’
Plastics are semi-organic and always derived from oil or petroleum
  Plastics are synthetic materials. What is meant by synthetic?

## Slide 4
The origins of plastics
Different polymers are derived from different sources
These can produce different types of plastics:
  Natural plastics made from rubber or latex
  Bio-plastics made from vegetable starches or algae
  Synthetic plastics made from petrochemical sources

## Slide 5
Natural plastics
There are some naturally occurring plastics:
  Amber (fossilised tree resin) and
  Latex (a form of rubber)
Natural latex is harvested from the Rubber tree (Hevea Brasiliensis)
  The bark is scored (tapped) to allow the milky sap to run out into a container

## Slide 6
Bioplastics
These are commonly made from corn or vegetable starches
  Fully biodegradable if composted
  Bacteria in the soil breaks down the plastic quickly
However, they cannot be recycled in a traditional way
  Why not?

## Slide 7
Synthetic plastics
Synthetic plastics are made from polymers
  These come from finite petrochemical resources; usually crude oil
  Plastics can also be derived from natural gas and coal

## Slide 8
Producing polymers
Polymers are produced through a lengthy process called refining
  Unprocessed (crude) oil is first extracted from underground, either at sea using an oil rig, or on land
  It is then transported to a plant for conversion

## Slide 9
Refining crude oil
Heavy, sticky black crude oil is virtually unusable in its unrefined state
  It has to be converted and refined into other more useable products such as fuels

## Slide 10
Fractional distillation
Fractional distillation occurs when crude oil is heated in the crude oil distillation unit
  Each product has different sized molecules with different boiling points
  How can this be used to separate petrol from diesel?

## Slide 11
Fractional distillation process
The different stages are:
  Crude oil is heated to 350°C
  Hot oil is pumped into the base of the distillation tower
  The crude oil vaporises and rises up the tower
  As the crude oil cools, the molecules condense
  Heavier molecules stay at the bottom and lighter molecules rise to the top
  The fractions (hydrocarbons) are siphoned off for cracking

## Slide 12
Fractional distillation
Complete Task 1 on Worksheet 1 to explain the different stages of fractional distillation

## Slide 13
Cracking
This is the process of converting the large hydrocarbon molecules found in the separated fuel types into smaller, more useful versions
  The large molecules do not flow very well and are not suitable to be converted into plastics
  Heat and pressure are used to break them up

## Slide 14
Polymerisation
After hydrocarbons are obtained from cracking, they are then chemically processed:
  Molecules of single compounds known as monomers join together
  These atoms are joined end to end to form long chains
  The long chains of molecules are called polymers
  MONO (one)    POLY (many)
  Polymers are the building blocks of all plastics

## Slide 15
Categories of plastic
There are two categories of plastic:
  Thermoplastics and
  Thermosetting plastics
Each type is dependent on the end molecular structure after polymerisation
  Polymers are usually in the form of pellets or beads
  These can then be processed into different forms, such as sheets, bars, pipes, films and fibres

## Slide 16
Thermoplastics
Thermoplastics are the most commonly used type
  They have long chains of molecules, tangled together with no fixed structure or pattern
  They are generally soft and flexible with shape memory

## Slide 17
Thermosetting plastics
Thermosets are more brittle than thermoplastics and are best suited to stiffer mouldings
  They have long chains of molecules, cross-linked that form a very rigid molecular structure
  Very hard and waterproof when solid - ideal for adhesives

## Slide 18
Plastic additives
Plastic can be adapted for different applications by adding chemicals, additives and compounds during manufacture
  Stabilisers help to make it more heat and light (UV) resistant
  What effect does UV light have on plastic?

## Slide 19
Pigments are added to change the colour of plastic
Plasticisers are added to make it more flexible
  In what applications are fragrances added to plastics?
  Where would antibacterial additives be helpful?
Tailoring plastics for use

## Slide 20
Why are plastics so affordable?
They are cheaper than similar products made from wood or metal because:
  They have a very high strength-to-weight ratio and many versatile properties
  The raw materials are cheaper
  Less energy is needed to make the products than other materials
  Products are easily mass produced
  Transport and fuel costs are less – why?

## Slide 21
Ethical issues in production
Negatives to manufacturing synthetic plastics:
  Producing polymers uses crude oil – a finite resource
  Produces pollutants – bad for the environment
  Processing polymers requires energy – global warming
  Some carcinogenic toxins found in PVC
  Is this acceptable? Can we live without plastics?

## Slide 22
Plastics in use
Plastic is seen as a disposable item by consumers
  Low cost leads to a throwaway culture (e.g. packaging)
  Plastic straws and cotton buds are only used once – what else could they be made from?
  Plasticisers used in contact with foodstuffs can leach chemicals into the food – should they continue to be used?
  How does this apply to plastic medical supplies?

## Slide 23
Ethical issues at end of life
What problems are caused by throwing plastics away rather than recycling or reusing them?

## Slide 24
Ethical issues at end of life
Plastics products do not rot or corrode easily but are often thrown away as landfill
  By ending up on landfill this adds to greenhouse gases
  Scars the landscape - countryside, rivers and oceans
  Discarded plastic bags affect marine life and coral reefs. They are often ingested by birds and fish
  Poisonous incineration - if burnt they produce black choking gases
  Toxins from microscopic plastic particles can enter the food chain and affect marine life and human health

## Slide 25
Recycling plastics
Thermoplastics can be recycled
  This reduces the disposal problems (landfill) and the amount of virgin crude oil used
  The different types of polymers must be separated from each other first – how simple do you think this is?
  They can also be recovered through Energy from Waste incineration (EfW) to provide electricity
Roads are now being made with recycled plastic instead of bitumen
  They are much more durable, quicker to lay and allow for better drainage

## Slide 26
How sustainable are plastics?
Almost all plastics are recyclable or biodegradable in some form
  Thermoplastics can be recycled by melting them down and reforming their shape into new products
  However, their usefulness can become limited with frequent reheating and reforming
  Can we make plastics more sustainable?

## Slide 27
Sustainable plastic production
Bio plastics are produced from vegetable starches such as corn
  What issues might there be with corn being grown specifically for making plastic?

## Slide 28
Modern bioplastics
BiopolTM can be manufactured from plant sugars and glucose from soya, pea or potato starches

## Slide 29
Bioplastics
Polylactic Acid (PLA) – Extracts carbon from plants
  A biodegradable plastic made from corn starch
Polycaprolactone (PCL) – e.g. Polymorph
  Low melting point, good modelling plastic
Polyhydroxybutyrate (PHB) – Biopol™
  Non-toxic, insoluble in water, high melting point

## Slide 30
Sustainability of plastics
Watch Link Video Sustainability on the life cycle of plastic bottles
Complete Tasks 2 and 3 of the worksheet

## Slide 31
Nylon – Thermoplastic
Can be woven into fabrics
Resilient to wear
Low friction
Tough
  What else is made from Nylon?

## Slide 32
The future of plastics?
We need to find other alternatives to petrochemicals to produce plastic. Some interesting developments include exploration of:
  Bioplastics (using corn starch)
  Algae (high growth rate) Latex
  Castor oil
  Plant-oil derived
  Fermentation of monomers
  Protein derived – e.g. chicken feathers

## Slide 33
Key terminology
Check that you understand the following:
  Fossil fuels
  Polymers
  Thermoforming polymers / Thermoplastics
  Thermosetting polymers / Thermosets
  Cracking
  Fractional distillation
  Bioplastics

## Slide 34
Match up the correct terms
Key word |  | Definition
Polymerisation |  | When thermoplastics are reheated they try to return to their original shape
Plastic memory |  | Plastics which soften when heated, harden when cooled and can be softened again numerous times
Thermosets |  | Finite resources such as oil, gas and coal which are used to make petrochemicals
Polymers |  | Plastics which soften when heated, harden when baked but won’t change shape when reheated
Fossil fuels |  | The name for monomers when joined together to form long chains of molecules
Thermoplastics |  | Polymers are chemically processed to join together
Cracking |  | Large hydrocarbons are converted into smaller, more useful versions using heat and pressure

## Slide 35
Answers
Key word |  | Definition
Polymerisation |  | When thermoplastics are reheated they try to return to their original shape
Plastic memory |  | Plastics which soften when heated, harden when cooled and can be softened again numerous times
Thermosets |  | Finite resources such as oil, gas and coal which are used to make petrochemicals
Polymers |  | Plastics which soften when heated, harden when baked but won’t change shape when reheated
Fossil fuels |  | The name for monomers when joined together to form long chains of molecules
Thermoplastics |  | Polymers are chemically processed to join together
Cracking |  | Large hydrocarbons are converted into smaller, more useful versions using heat and pressure